Tuesday, January 21, 2003

ENEL 699  Review

The Fourier Transform of a Windowed Gate Function

This document is intended to assist you in reviewing some of the prerequisite undergraduate material and also to become familiar with Matlab as a tool for studying signal processing.  You are not required to submit this work.

Consider the continuous-valued continuous-time-domain gate signal function

,

where  is the unit step function.

- Employing a uniform sample rate of at least 100 samples per second (), obtain the uniformly-sampled infinite-duration version , , of this signal in Matlab.

In order to employ a finite number of samples within Matlab, you will need to employ a multiplicative window function  to yield a finite-duration domain signal  of duration prior to sampling and it is suggested you use

and  be not less than 10 times the ROS of the continuous-domain signal in .

- Use the Matlab DFT function to plot the magnitude DFT of the sampled signal

- Compare the result in 2 above with the magnitude Fourier transform  (i.e. magnitude spectrum) of the original continuous-domain signal in , plotting them on the same graph with appropriate choices for the scales of  and .

- Why does the discrete transform  not lie exactly on the curve  ?  How does the difference between them change as a function of  and of  ?  What are the engineering implications of your answers ?

- Explain how the above answers change if the signal in  is delayed by 1 second.

- Use a different type of window function in Matlab (e.g. Hanning) and explain the new results.

- Investigate the effects (on the time-domain inverse DFT) of removing the highest coefficients of the DFT .   Explain the engineering relevance and the theory of this operation.

- How does the bandwidth of a gate signal depend on the duration (ROS) of the gate.

- If the discontinuities of the gate function are converted to linear ramps so as to more realistically describe an actual electronic pulse, how will this effect the magnitude spectrum of the signal?